## Slide 1: Superconductors, light, and the “age of of cognition”
Jeff Chiles, Sonia Buckley, Adam McCaughan, Saeed Khan, Bryce Primavera,
Rich Mirin, Sae Woo Nam, Jeff Shainline
NIST, Physical Measurement Laboratory
“Super” Neuromorphic Computing with Photonic and Superconducting Devices

## Slide 2: High Performance Single Photon Detectors
Superconducting nanowire single photon detector
Superconducting Transistion-Edge Sensors
Microwave Kinetic Inductance Detectors
Conventional Applications
  Advanced sensors for astronomy and astrophysics
  High Energy Physics – rare particle event searches
  Quantum Information / Quantum Computation

## Slide 3: Photonic Quantum Information Requirements
 | Quantum Communication | Quantum Computing (Photonic) | Quantum Computing (atoms) | Entanglement-based random numbers
Wavelength | 1550 nm | Visible, Near-IR | UV | Near-IR
Detection Efficiency | As high as possible | As high as possible | >80% | >67%
Dark / Background counts | As low as possible
Timing jitter | As low as possible
Maximum count rate | As high as possible

## Slide 4: Conventional Single-Photon Detectors
Commercially available
Relatively inexpensive
M. D. Eisaman, J. Fan, A. Migdall, and S. V. Polyakov, Rev. Sci. Instrum. 82, 071101 (2011)

## Slide 5: Low Temperature Physics = High Performance
No afterpulsing problems
Excellent prospects for longer wavelengths
TES: Transition Edge Sensor
SNSPD: Superconducting Nanowire Single Photon Detector

## Slide 6: Superconducting Nanowire Single Photon Detectors:
ultra-thin (2nm to 8nm)
Anomolous kinetic inductance
NbN, NbTiN
  2K operating temperature
  ~80nm wide
New materials:
W-Si, Mo-Si, Mo-Ge
  1K operating temperature
  ~150nm
5 microns wide

## Slide 7: Simplicity of Superconducting Nanowire Single Photoncs Detectors
X
Simple Readout
Bias versus Efficiency / counts

## Slide 8
Air
aSi
SiO2
aSi
SiO2
Au
Substrate
Incoming photons
Single Pixel Devices
2.5 mm
Available Commercially now !!!
60 nm
100 nm
Notes: 8

## Slide 9: Future of Computing
High Performance Computing. (HPC)
  Traditional model of computation
Quantum Computing and Networking (QC)
  Can outperform HPC in some tasks
Neuromorphic Computing (NC)
  “Neuroscience” inspired architecture
  Dedicated Hardware

## Slide 10: Structure of a Biological Neuron
https://www.khanacademy.org/science/biology/human-biology/neuron-nervous-system/a/the-synapse
http://spie.org/news/5681-dendritic-plateau-potentials-modulate-neuronal-function?SSO=1
From:Wikipedia
DENDRITES

## Slide 11: Fast Introduction to Neural Networks
Artificial Neuron
Network of Neurons
http://www.asimovinstitute.org/neural-network-zoo/
Input Cell / Layer
Hidden Cell / Layer
Output Cell / Layer
S
F(x)
w1
w2
w3
x1
x2
x3
b
Summing
Node
Synaptic
Weights
inputs
Activation
Function

## Slide 12: Supervised Learning
Untrained
Neural Network
cat
not
cat
✅
Trained
Neural Network
Inference
New
Data
Training
✓
✓

## Slide 13: Machine learning hardware
Today, there is large demand to perform “neural network” operations
  Image Classification
  Speech Recognition
  Natural Language Processing: “translation”
Dedicated Neuromorphic Hardware
Other Technology platforms Neuromorphic have attracted venture interest
Bill Gates
TrueNorth, IBM
see Merolla et al.,
Science, 2011.
Notes: Plug Nick’s talk
I don’t have to make a case that Moore’s law is ending. There is a belief that electronics will not be able to supply what is needed – nothing is on the way. This was not true in 1980s. GPUs and FPGAs

## Slide 14
2nd and 3rd Generation Neural Networks
2nd Generation: “Proven”
Limited Biological “inspiration”
Matrix-vector multiplication
Seeking weight matrix
Trained by supervisory system
Limited History
Task specific
3rd Generation: “Less Proven”
More Biologically inspired
Information in dynamical state
Spiking neurons communicate in rate and timing
Potential for learning without supervision
Information integrated across space and time
General cognitive systems

## Slide 15: Question: Why do we need Generation 3? Answer: Energy Efficiency and Size
https://arxiv.org/abs/1906.02243v1
“How do you make the largest scale artificial neural network?”
  Human Brain:
    10 billion neurons
    1 neuron fans out to 10,000 neurons
What are the fundamental limits?
How do you evaluate the performance?
How do physical characteristics of the devices relate to the performance of the neuromorphic computer?

## Slide 16: Spiking Neural Networks / Dedicated Hardware
Biologically Inspired
  Spiking Signals, Energy Efficient
  Rate and Time encoding
Differentiated local processing
Information integration across:
  Space (network structure)
  Time (dynamics)
  Experience (plasticity)
Can we get to a size scale for “Cognitive” Systems?

## Slide 17: Energy and Training Targets
Power
2500 kCal/day = 100Watts
Clock speed
1 Hz to 1kHz
Training time
18 years
Power
100 kW to 1 MW
Clock speed
1 Mhz to 10MHz
Training time
1 week
Human
Artificial
Notes: Dominated by light source
1fJ is needed per synapse
10^10 neurons * 10^4 connections * 1fJ / 10^-4 efficiency of the source = 10^3 Joules
10^6 clockspeed * 10^-3 utilization (not all neurons firing at once) = 1Mwatt

## Slide 18: Energy estimates
10^10 neurons
10^10 * 10^4 connections
10^10 * 10^4 * 10^5 photons
10^19 photons * 10^4 inefficiency
10^23 photons = 10^23 eV = 10^4 J
1fJ = 1e-15J = 10 photons

## Slide 19
Fluxonic processing of photonic synapse events
Spiking neural networks
jeffrey.shainline@nist.gov

## Slide 20
Fluxonic processing of photonic synapse events
Light for communication

## Slide 21
Fluxonic processing of photonic synapse events
Superconducting electronics for single-photon detection

## Slide 22
Fluxonic processing of photonic synapse events
Superconducting electronics for neural computation

## Slide 23
Fluxonic processing of photonic synapse events
Neuromorphic supercomputing

## Slide 24
Device requirements for massive connectivity
Dense local fanout
Long-range connectivity
Principal conjecture:
Use light for communication
Photons don’t have charge or mass
We seek very large systems
Energy efficiency is paramount
Use single-photons for communication

## Slide 25
Neurons that signal with single photons

## Slide 26
Neurons that signal with single photons
How do they work?

## Slide 27
Superconducting loop

## Slide 28
Photons add current

## Slide 29
Current gets integrated

## Slide 30
Current threshold

## Slide 31
Current threshold

## Slide 32
Photons produced

## Slide 33
Synapse transduces

## Slide 34
Photons update weight

## Slide 35
Inhibitory synapses

## Slide 36
Many synapses

## Slide 37
Transmitter circuits

## Slide 38
Colors for different operations

## Slide 41
Loop neuron
Shainline et al., arXiv:1805.01929 (2018).
Shaineline, arXiv:1904.02807 (2019)

## Slide 42
Photon-to-fluxon transducer
these are fluxons

## Slide 43
The synapse

## Slide 44
Long-range = photons
Short-range = electronics / SFQ
https://arxiv.org/abs/1907.00263
A Power Efficient Artificial Neuron Using Superconducting Nanowires
Emily Toomey, Ken Segall, Karl Berggren
Pulsed neural networks consisting of single-flux-quantum spiking neurons
T. Hirose, T. Asai, and Y. Amemiya
Physica C, 463:1072, 2007.

## Slide 45: SOEN technical approach superconducting optoelectronic networks
Single photons for minimum spike energy
  (superconducting single-photon detectors )
2. Cold optoelectronics for monolithic integration
  (all-silicon light-emitting diodes)
3. Cold electronics (SFQ) for nonlinear processing
  (Josephson junctions, cryotron switches)
4. Light for interconnects
  (silicon photonics)
1.
2.
3.
4.
J. M. Shainline, S. M. Buckley, R. P. Mirin, and S. W. Nam, “Superconducting optoelectronic circuits for neuromorphic computing,” Phys. Rev. Applied, Mar 2017.
Notes: Accepting to work at cryogenic temperatures means other devices become available

## Slide 46: cryogenic silicon photonics platform: recent results

## Slide 47
Superconducting Nanowire Detector
single photon
160 nm
5 nm
Waveguide
Nanowire on waveguide

## Slide 48: All-silicon light emitting diodes
Si defect centers have optical transitions
Low temp. inhibits non-radiative pathways
Electrical pumping with PN junction
W-centers: 1220nm emission
S. M. Buckley et al. “All-silicon light-emitting diodes waveguide-integrated...” APL, 2017.
Notes: Describe the fabrication briefly

## Slide 49: Co-integration: Silicon LEDs + SNSPDs
S. M. Buckley et al. “All-silicon light-emitting diodes waveguide-integrated...” APL, 2017.
Notes: Say that: since this article, we have enhanced photoluminescence by a factor of 300. Promising results and a paper is in preparation.

## Slide 50: All-silicon light emitting diodes
LED turn-on voltage is ~ 1 V
SNSPD can output ~ 1 mV
S. M. Buckley et al. “All-silicon light-emitting diodes waveguide-integrated...” APL, 2017.
Notes: Describe the fabrication briefly

## Slide 51: Nano-cryotron thermal switch
millivolt input -> Volt output
No Josephson Junctions needed
Reset about 10ns
A. McCaughan et al. “A compact, ultrahigh impedance superconducting thermal switch for interfacing superconductors with semiconductors and optoelectronics,” arXiv:1903.10461, 2019.

## Slide 52: Superconductor-to-semiconductor interface
4.6 us
Time (us)
A. McCaughan et al. “A compact, ultrahigh impedance superconducting thermal switch for interfacing superconductors with semiconductors and optoelectronics,” arXiv:1903.10461, 2019.
Notes: What points to make about this

## Slide 53: First steps toward photonic networks
Three planes of amorphous silicon waveguides
Chiles et al., APL Photonics 2, 116101 (2017)

## Slide 54
Inter-planar couplers
0.05 dB loss
36 mm length
36 mm
Chiles et al, APL Photonics 2 116101 (2017).

## Slide 55
10 x 100 routing couplers
Chiles et al, APL Photonics 3 106101 (2018).

## Slide 56
10 x 100 routing couplers

## Slide 57
10 x 100 routing couplers

## Slide 58: Full Superconducting Optoelectronic Neuron
Optical
Optical
Fluxonic
SNSPDs
Silicon LED
Josephson
Junction circuits
Electronic
Electronic
Superconducting
Switch
J. M. Shainline, “Fluxonic processing of photonic synapse events,” arXiv:1904.02807, 2019.
Notes: photons are expensive
one circuit multiple purposes (enumerate some)
summing and intermediate processing
Come back to characteristic length. We should pack a bunch of complexity in a small space and make it electronic

## Slide 59: Eventual transfer to 300 mm foundry
Notes: And for better scale

## Slide 60
Fabricated at SUNY Poly by Pops Papa Rao and team
Measured at NIST by our team
Light sources on 300-mm wafers
Photoluminescence of W centers in Si at 4 K

## Slide 61
Wafer-scale modules

## Slide 62: Free-space interconnects for 3D

## Slide 63
Free-space inter-wafer interconnects

## Slide 64
Multi-wafer modules

## Slide 65
Brain-scale systems?
> 100 Billion neurons

## Slide 66
What can we do in five years?
Artificial visual cortex

## Slide 67
Dense local fan-out with photonics
Long-range communication at light speed
Computing and memory with superconducting electronics
Superconducting
optoelectronic
networks
Would this reach the limits of cognition?

## Slide 69: Summary
Low Temperature Devices have the potential to be important in super-neuromorphic computing
Can we get to a size scale for “Cognitive” Systems?
Light for communication
Superconductors for computation
Complex neuro circuits

## Slide 70: NIST team
Rich Mirin
Jeff Shainline
Sonia Buckley
Adam McCaughan
Alex Tait
Jeff Chiles
Saeed Khan
Krister Shalm
Marty Stevens
Adriana Lita
Varun Verma
Nima Nader
Mike Mazurek
Dileep Reddy
Eric Stanton
Galen Moody
Kevin Silverman
Thomas Gerrits
Boulder Labs
saewoo.nam@nist.gov
MIT, JPL, Suny-Poly